Bat Wing Installation

Savior 250psi installation instructions. Part # 42739-7867

Harley FLH Bat wing model from 1995 to 2008

- Remove fairing ref. To page 2-92 Harley shops manual.

- Detach right handlebar switch control harness from bracket no need to disconnect.

- Loosen left screw remove right screw and remove original H-D support bracket.

- Install compressor loosely on new bracket. Attach the short black wire from the compressor to the right screw on the mounting bracket. Re install the new bracket and adjust compressor to clear motor vent. Make sure throttle cable don't touch large white gear. The cable will fit in a grove just under the gear housing. Tighten left and re-install right screw. Tighten clamp screw. Re-attach right handlebar switch control harness to new bracket pin.

- From main gray interconnect harness. Accessory switch could be tap in at the solid orange wire splice and connect Red or Light brow wire from compressor. black wire to instrument black ground.

- 5A) Optional If using switch part # 5051 go directly to available power source on the cigarette lighter  black to ground red to hot or  to a 15 amp fused circuit Drill 1/2 hole through inner fairing most suitable to your discretion. Unplug red or light brown wire. Tread switch wires through hole tighten nut re-plug wires.

- Drill 5/16 hole through front inner fairing.  Use hose to set distance from compressor. This is the most suitable location, it does not interfere with the rotation of steering.  It Can also be installed at the bottom part of the inner fairing.

- Turn switch on to Test compressor.

- Re install fairing.